## Slide 1: Microprocessor Cortex-M3 Instruction Set
Seung-Ho Lim
Hankuk University of Foreign Studies

## Slide 2: Agenda
Assembly Basics
Endian format
Cortex-M3 Registers & Memory
Corex-M3 Instruction Set Architecture

## Slide 3: Assembly Basics
Assembler Language: Basic Syntax
  Common format for assembler code
  Label
    The address of the instructions can be determined using the label
  Opcode
    Encoded symbol of instruction that let processor execute
  Operands
    Values or registers to be executed by opcode
  Comments
    Additional explain for the statements. Identified by ;
label
opcode operand1, operand2, ...; Comments

## Slide 4: Assembly Basics
Assembler Language examples
    Opcode, operands, comment
  Define constant using EQU (similar to #define in c)
MOV R0, #0x12 ; Set R0 = 0x12 (hexadecimal)
MOV R1, #'A' ; Set R1 = ASCII character A
NVIC_IRQ_SETEN0 EQU 0xE000E100
NVIC_IRQ0_ENABLE EQU 0x1
...
LDR R0,=NVIC_IRQ_SETEN0; ; LDR here is a pseudo-instruction that
; convert to a PC relative load by
; assembler.
MOV R1,#NVIC_IRQ0_ENABLE ; Move immediate data to register
STR R1,[R0] ; Enable IRQ

## Slide 5: Assembly Basics
Assembler Language: Use of Suffixes
  In assembler for ARM processors, instructions can be followed by suffixes
  The conditional execution suffixes are usually used for branch instructions

## Slide 6: The Endianess religious war: 288 years and counting!
Modern version
  Danny Cohen
  IEEE Computer, v14, #10
  Published in 1981
  Satire on CS religious war
Historical Inspiration
  Jonathan Swift
  Gulliver's Travels
  Published in 1726
  Satire on Henry-VIII’s split with the Church
    Now a major motion picture!
Memory Value
Offset (LSB) (MSB)
====== ===========
uint8_t a = 1; 0x0000 01 02 FF 00
uint8_t b = 2;
uint16_t c = 255; // 0x00FF
uint32_t d = 0x12345678; 0x0004 78 56 34 12
Little-Endian
  LSB is at lower address
Big-Endian
  MSB is at lower address
Memory Value
Offset (LSB) (MSB)
====== ===========
uint8_t a = 1; 0x0000 01 02 00 FF
uint8_t b = 2;
uint16_t c = 255; // 0x00FF
uint32_t d = 0x12345678; 0x0004 12 34 56 78

## Slide 7: Addressing: Big Endian vs Little Endian
Endian-ness: ordering of bytes within a word
  Little - increasing numeric significance with increasing memory addresses
  Big – The opposite, most significant byte first
  MIPS is big endian, x86 is little endian

## Slide 8: ARM Cortex-M3 Memory Formats (Endian)
Default memory format for ARM CPUs: LITTLE ENDIAN
Bytes 0-3 hold the first stored word
Bytes 4-7 hold the second stored word
Processor contains a configuration pin BIGEND
  Enables system developer to select format:
    Little Endian
    Big Endian (BE-8)
  Pin is sampled on reset
  Cannot change endianness when out of reset
Source: [ARM TRM] ARM DDI 0337E, “Cortex-M3 Technical Reference Manual,” Revision r1p1, pg 67 (2-11).

## Slide 9: Instruction Set Architecture
Instruction Set
  The complete details of each instruction are available in the ARM v7-M Architecture Application Level Reference Manual
Cortex-M3 Instruction Type
  16-bit/32-bit Data Processing Instructions
  Branch Instructions
  16-bit/32-bit Load and Store Instructions
  Etc.
    Coprocessor instructions

## Slide 10: An ISA defines the hardware/software interface
A “contract” between architects and programmers
Register set
Instruction set
  Addressing modes
  Word size
  Data formats
  Operating modes
  Condition codes
Calling conventions
  Really not part of the ISA (usually)
  Rather part of the ABI
  But the ISA often provides meaningful support.

## Slide 11: ARM Cortex-M3 ISA
Register Set
Address Space
Branching
Data processing
Load/Store
Exceptions
Miscellaneous
Instruction Set
32-bits
32-bits
Endianess
Endianess

## Slide 12: Registers for ISA
Mode dependent
SP_main (MSP) used by:
OS kernel
Exception handlers
App code w/ privileded access
SP_process (PSP) used by:
Base app code (when not running an exception handler)
Note: there are two stack pointers!

## Slide 13: Address Space

## Slide 14: ARM Instruction Set Architecture
32-bits
32-bits
Endianess
mov r0, #4
ldr r1, [r0,#8]
r1=mem((r0)+8)
bne loop
subs r2, #1
Endianess

## Slide 15: Instruction Descriptions Details
1) Assembler Language: Moving Data
  One of the most basic functions in a processor is transfer of data.
  In the Cortex-M3, data transfers can be of one of the following types:
    Moving data between register and register
      Ex) MOV R8, R3
    Moving data between memory and register
      Ex) STMIA.W R8!, {R0-R3}
    LDR.W R0, [R1, #offset]!
    Moving data between special register and register
      Ex) MRS R0, PSR
    Moving an immediate data value into a register
      Ex) MOVS R0, #0x12

## Slide 16: Instruction Descriptions
2) Assembler Language: Processing Data
  Processing data means Addition, Subtraction, Multiply, Division
  Aside from ADD instructions, the arithmetic functions that the Cortex-M3 supports include subtract (SUB), multiply (MUL), and unsigned and signed divide (UDIV/SDIV).
  Addition
    ADD R0, R0, R1 ; R0 = R0 + R1
    ADDS R0, R0, #0x12 ; R0 = R0 + 0x12
    ADD.W R0, R1, R2 ; R0 = R1 + R2
  Subtraction
    SUB R0, R0, R1 ; R0 = R0 - R1
    SUBS R0, R0, #0x12 ; R0 = R0 - 0x12
    SUB.W R0, R1, R2 ; R0 = R1 - R2
  Multiply
    MUL Rd, Rm ; Rd = Rd * Rm
    MUL.W Rd, Rn, Rm ; Rd = Rn * Rm
  Division
    UDIV Rd, Rn, Rm ; Rd = Rn/Rm
    SDIV Rd, Rn, Rm ; Rd = Rn/Rm

## Slide 17: Instruction Descriptions
3) Assembler Language: Call and Unconditional Branch
  Jump to the specified address that is expected to be executed
    B label ; Branch to a labeled address
    BX reg ; Branch to an address specified by a register
4) Assembler Language: Combined Compare and Conditional Branch
  a simple compare with zero and conditional branch operations.
    CBZ (compare and branch if zero)
    CBNZ (compare and branch if nonzero).

## Slide 18: Instruction Descriptions Details
Four Type of Instructions
  Assembler Language: Moving Data
    Data moving from resisters to registers
    Data moving from registers to memory
  Assembler Language: Processing Data
    Data arithmetic operations
    Data logical operations
  Assembler Language: branch
    Call and Unconditional Branch
    Combined Compare and Conditional Branch
    program flow control
  Assembler Language: Use of Suffixes

## Slide 19: Instruction Descriptions Details
1) Assembler Language: Moving Data
  One of the most basic functions in a processor is transfer of data.
  In the Cortex-M3, data transfers can be of one of the following types:
    Moving data between register and register
      Ex) MOV R8, R3
    Moving data between memory and register
      Ex) STMIA.W R8!, {R0-R3}
    LDR.W R0, [R1, #offset]!
    Moving data between special register and register
      Ex) MRS R0, PSR
    Moving an immediate data value into a register
      Ex) MOVS R0, #0x12

## Slide 20: Assembler Language: Moving Data
Load/Store instructions

## Slide 21: Addressing Modes
Offset Addressing
  Offset is added or subtracted from base register
  Result used as effective address for memory access
  [<Rn>, <offset>]

## Slide 22: Addressing Modes
Pre-indexed Addressing
  Offset is applied to base register
  Result used as effective address for memory access
  Result written back into base register
  [<Rn>, <offset>]!
    The exclamation mark (!) in the instruction specifies whether the value should be updated
  Example

## Slide 23: Addressing Modes
Post-indexed Addressing
  The address from the base register is used as the EA
  The offset is applied to the base and then written back
  [<Rn>], <offset>
  Example

## Slide 24: Multiple load/store
Multiple Load and Store operations can be combined into single instructions called LDM (Load Multiple) and STM (Store Multiple)
The exclamation mark (!) in the instruction specifies whether the register Rd should be updated after the instruction is completed

## Slide 25: Instruction Descriptions
2) Assembler Language: Processing Data
  Processing data means Addition, Subtraction, Multiply, Division
  Aside from ADD instructions, the arithmetic functions that the Cortex-M3 supports include subtract (SUB), multiply (MUL), and unsigned and signed divide (UDIV/SDIV).
  Addition
    ADD R0, R0, R1 ; R0 = R0 + R1
    ADDS R0, R0, #0x12 ; R0 = R0 + 0x12
    ADD.W R0, R1, R2 ; R0 = R1 + R2
  Subtraction
    SUB R0, R0, R1 ; R0 = R0 - R1
    SUBS R0, R0, #0x12 ; R0 = R0 - 0x12
    SUB.W R0, R1, R2 ; R0 = R1 - R2
  Multiply
    MUL Rd, Rm ; Rd = Rd * Rm
    MUL.W Rd, Rn, Rm ; Rd = Rn * Rm
  Division
    UDIV Rd, Rn, Rm ; Rd = Rn/Rm
    SDIV Rd, Rn, Rm ; Rd = Rn/Rm

## Slide 26: Assembler Language: Processing Data
Examples of Arithmetic Instructions

## Slide 27: Assembler Language: Processing Data
32-Bit Multiply Instructions

## Slide 28: Assembler Language: Processing Data
Logic Operation Instructions

## Slide 29: Assembler Language: Processing Data
Shift and Rotate Instructions

## Slide 30: Assembler Language: Processing Data
Shift and Rotate Instructions

## Slide 31: Assembler Language: Processing Data
Many, Many More!
More on

## Slide 32: Instruction Descriptions
3-1) Assembler Language: Call and Unconditional Branch
  Jump to the specified address that is expected to be executed
    B label ; Branch to a labeled address
    BX reg ; Branch to an address specified by a register
3-2) Assembler Language: Combined Compare and Conditional Branch
  a simple compare with zero and conditional branch operations.
    CBZ (compare and branch if zero)
    CBNZ (compare and branch if nonzero).

## Slide 33: Branch

## Slide 34: Branch examples
b label
  Branch without link (i.e. no possibility of return) to label
  The PC is not saved!
bx reg
  Use to return from a function
  Generally, lr is used for reg
  Moves the lr value into the pc
  Could be a different register than lr as well

## Slide 35: Branch examples
bl label
  Branch with link (call) to function label
  Store the return address in the link register (lr)
blx reg
  Branch to address specified by reg
  Save return address in lr
  When using blx, makre sure lsb of reg is 1 (otherwise, the CPU will fault b/c it’s an attempt to go into the ARM state)

## Slide 36: Branch examples
Bx label, blx label
  But since Cortex M-3 does not support ARM state, this instruction causes a fault!
Without branch instruction, branch is possible
  Use MOV and LDR

## Slide 37: Branch examples
Calling bl overwrites contents of lr!
So, save lr if your function needs to call a function!

## Slide 38: Conditional Branch
Most conditional branches in ARM processors use flags in the APSR to determine whether a branch should be carried out.
In the APSR, there are five flag bits; four of them are used for branch decisions

## Slide 39: Flags in ARM Processors
Data processing instructions change the flags in the PSR
The flags might be used for branch decisions
Z (Zero) flag:
  This flag is set when the result of an instruction has a zero value or when a comparison of two data returns an equal result.
N (Negative) flag:
  This flag is set when the result of an instruction has a negative value (bit 31 is 1).
C (Carry) flag:
  This flag is for unsigned data processing—for example, in add (ADD) it is set when an overflow occurs; in subtract (SUB) it is set when a borrow did not occur (borrow is the invert of carry).
V (Overflow) flag:
  This flag is for signed data processing; for example, in an add (ADD), when two positive values added together produce a negative value, or when two negative values added together produce a positive value.

## Slide 40: Application Program Status Register (APSR)

## Slide 41: Use of Suffixes
4) Assembler Language: Use of Suffixes
  In assembler for ARM processors, instructions can be followed by suffixes
  The conditional execution suffixes are usually used for branch instructions

## Slide 42: Use of Suffixes
Conditions for Branches or Other Conditional Operations

## Slide 43: Updating the APSR
SUB Rx, Ry
  Rx = Rx - Ry
  APSR unchanged
SUBS
  Rx = Rx - Ry
  APSR N, Z, C, V updated
ADD Rx, Ry
  Rx = Rx + Ry
  APSR unchanged
ADDS
  Rx = Rx + Ry
  APSR N, Z, C, V updated

## Slide 44: Use of Suffixes
Examples of using of Suffixes

## Slide 45: Exercise: What is the value of r2 at done?
...
start:
movs r0, #1
movs r1, #1
movs r2, #1
sub r0, r1
bne done
movs r2, #2
done:
b done
...

## Slide 46: Summary
Cortex M-3 Instruction Set Architecture
Cortex M-3 Instruction details
  Data moving
  Data processing
  Branch
  Use suffixes