## Slide 1: Microprocessor Introduction
Seung-Ho Lim
Hankuk University of Foreign Studies

## Slide 2: Class Information
Instructor:
  Seung-Ho Lim
  E-mail : slim@hufs.ac.kr
  Office : Engineering Building 417
  Lecture hours : Wednesday 78, Friday 56
Teaching Assistant
  Sohoon Jin
Course Objective:
  Interpret and design hardware and software for simple digital systems
  which use Cortex-M3 microcontroller
  Study the fundamentals of microprocessor organization and operation
  Assembly and C programming based on the Cortex-M3 microcontroller
  instruction set
  Study the basis for interaction between the Cortex-M3 microcontroller and
  external hardware with experiments

## Slide 3: Class Information
Lecture Book
  The Definitive Guide to ARM Cortex-M3, second edition
Lecture Contents
  Microprocessor & microcontrollers
  The ARM cortex-M3 microcontroller hardware details
  The ARM cortex-M3 instruction set
  The ARM cortex-M3 assembly/C programming
  GPIO Control, Interrupt, Timer, UART, Step Motor, KeyPAD, etc…
Grading:
  Mid-term exam – 37%
  Final exam – 38%
  HW/ Labs reports and experiments, projects – 20%
  Attendance – 5%

## Slide 4: Experimental Materials
HBE-MCU-Multi
  HBE-MCU-Multi 로 배우는 마이크로컨트롤러(cortex-M3)

## Slide 5: Class Tentative Schedule
Week | Wednesday
 | Friday
1 | (9/4) Introduction of the Course (Lec)
 | (9/6) Basic Computer Architecture, Overview of Cortex-M3 (Lec)
2 | (9/11) Basic Computer Architecture, Overview of Cortex-M3 (Lec)
 | (9/13) Holliday
3 | (9/18) Cortex-M3 ISA – Assembly Programming (Lec)
 | (9/20) Experimental Environment Setup & simple test labs (Lab)
4 | (9/25) Cortex-M3 ISA – Arithmetic and Logic (Lec)
 | (9/27) Cortex-M3 Microcontroller – Assembly Programming Labs (Lab)
5 | (10/2) Cortex-M3 ISA – Branch, Control, Memory Map (Lec)
 | (10/4) Cortex-M3 Assembly Programming – Arithmetic and Logic Labs (Lab)
6 | (10/9) Holliday
 | (10/11) Cortex-M3 Assembly Programming – Arithmetic and Logic Labs (Lab)
7 | (10/16) Cortex-M3 ISA & Cortex-M3 Memory Map, GPIO (Lec)
 | (10/18) GPIO Labs (Lab)
8 | Middle Exam

## Slide 6: Class Tentative Schedule
Week | Wednesday
 | Friday
9 | (10/30) Cortex-M3 Interrupt (Lec)
 | (11/1) Interrupt Labs (Lab)
10 | (11/6) Cortex-M3 Timer (Lec)
 | (11/8) Timer Labs(Lab)
11 | (11/13) Cortex-M3 Timer PWM (Lec)
 | (11/15) Timer PWM Labs(Lab)
12 | (11/20) Serial Port(Lec)
 | (11/22) UART(Serial) Labs (Lab)
13 | (11/27) Cortex-M3 TextLCD (Lec)
 | (11/29) Cortex-M3 TextLCD Labs (Lab)
14 | (12/4) Step Moter and KeyPAD (Lec)
 | (12/6) Step Moter and KeyPAD Labs (Lab)
15 | (12/11) Term Project
 | (12/13) Term Project Demo
16 | Final Exam

## Slide 7: Topics covered in this course
Introduction to microprocessor organization and operations, emphasizing the Comtex-M3 microcontroller subset.
Introduction to computer architecture, with emphasis on systems involving the Comtex-M3 microcontroller.
Machine and assembly language programming for the ARM Comtex-M3 and variants.
C language programming for embedded systems.

## Slide 8: By the end of the course,
You should be able to :
  Understanding the organization of a simple microcontroller.
  Analyze and design hardware and software for small digital systems involving microcontrollers.
  Program embedded computer systems in Assembly and C.
  Use the Comtex-M3 microcontroller and its standard peripherals.

## Slide 9: Why this course is important
Microcontrollers are use extensively in process control, instrumentation, home appliances, automobiles, etc.
They represents a basic building block of modern digital systems design.
If you go into virtually any form of engineering design, there is a high probability that knowledge of microcontrollers will be required.
Microcontrollers area the basis of embedded systems.

## Slide 10: Preliminarily studies
  Numbering for computer systems
  Digital primer
    Gates
    Decoder
    Mux
    register

## Slide 11: Numbering and Coding Systems
Human beings use base 10(decimal) arithmetic
  There are 10 distinct symbols, 0~9
Computers use base 2(binary) system
  There are only 0 and 1
  These two binary digits are commonly referred to as bit
converting from decimal to binary
  divide the decimal number by 2 repeatedly
  keep track of the remainders
  continue this process until the quotient becomes zero
  write the remainders in reverse order to obtain the binary number

## Slide 12: Numbering and Coding Systems
Converting from binary to decimal
  Know the weight of each bit in a binary number
  Add them together to get its decimal equivalent

## Slide 13: Numbering and Coding Systems
Hexadecimal system
  Base 16, the hexadecimal system, is used ad a convenient representation of binary numbers
  To represent a binary number as its equivalent hexadecimal number
    Start from the right and group 4 bits at a time
    replacing each 4-bit binary number with its hex equivalent

## Slide 14: Binary Logic
Two voltage levels can be represented as the two digits 0 and 1
Signals in digital electronics have two distinct voltage levels with built-in tolerances for variations in the voltage
A valid digital signal should be within either of the two shaded areas

## Slide 15: Very basic components of Computer
Logic Gates
  AND gate
  OR gate

## Slide 16: Very basic components of Computer
Logic gates
  Inverter
  XOR gate

## Slide 17: Very basic components of Computer
Logic gates
  NAND gate
  NOR gate

## Slide 18: Basic Digital Logic Components
Microprocessor composed of several digital Logic components
  Adder
  Decoder
  Mux(Multiplexor)
  Register
  Bus
  Etc.

## Slide 19: Digital Logic Design using Gates
Adder
  Adders are used for arithmetic operations of two operands

## Slide 20: Digital Logic Design using Gates

## Slide 21: Digital Logic Design using Gates
Decoders
  Decoders are widely used for address decoding in computer system

## Slide 22: Digital Logic Design using Gates
Flip-flops
  Flop-flops are frequently used to store data

## Slide 23: Digital Logic Design using Gates
Register
  3-dimensional flip-flops are register
  Stack 4 flip flops to get 4 bit data register
  Strobe clk(clock) to get D = Q

## Slide 24: Summary
Introduction to Coursework
Basic Computing System
Basic modules for microprocessor