## Slide 1: Microprocessor Basic Computer Architecture & Cortex-M3 Basics
Seung-Ho Lim
Hankuk University of Foreign Studies

## Slide 2: Organization of Computers
CPU (Central Processing Unit)
  Execute something stored in memory
Memory
  Temporary storage of program and data that CPU executes
I/O (Input/Output) Devices
  Provides a means of communicating with CPU

## Slide 3: Organization of Computers
The CPU is connected to memory and I/O through strips of wire called bus
Bus carries information from one to another
  Address bus
    used to assign a specific region or devices
  Data bus
    Use to transfer data from CPU to others, or vice versa
  Control bus
    Provides control signal from CPU to others, such as read or write

## Slide 4: Organization of Computers
(General Purpose)microprocessor VS. microcontroller
  GP microprocessor contains only processing unit inside it, and no RAM and other I/O devices
  Microcontroller has all in inside it, such as processing unit, RAM, ROM, I/O control units, and so on.

## Slide 5: ARM RISC Design Philosophy
Instructions
  A fixed size: 32-bit
  Executes in a single cycle
Pipelines
Registers
  A large general-purpose register set
Load-store architecture
Variable cycle execution for some instructions
  LDM/STM, SWP
Thumb 16-bit instruction set
Enhanced DSP instructions

## Slide 6: ARM Core Data Flow Model
Arithmetic
Logic
Load
Store

## Slide 7: ARM instructions

## Slide 8: What is the ARM Cortex-M3 Processor
ARM Cortex-M3 Processor
  32-bit microprocessor
Features of ARM Coretex-M3
  Greater performance efficiency
  Low power consumption
  Enhanced determinism
  Improved code density
  Ease of use
  Lower cost solutions

## Slide 9: Background of ARM
ARM was founded in 1990 as Advanced RISC Machines
  RISC (Reduced Instruction Set Computer) Architecture

## Slide 10: The Evolution of ARM Processor Architecture

## Slide 11: ARM is the big player
ARM has a huge market share
  As of 2011 ARM has chips in about 90% of the world’s mobile handsets
  As of 2010 ARM has chips in 95% of the smartphone market, 10% of the notebook market
    Expected to hit 40% of the notebook market in 2015.
  Heavy use in general embedded systems.
    Cheap to use
      ARM appears to get an average of 8¢ per device (averaged over cheap and expensive chips).
    Flexible
      Spin your own designs.

## Slide 12: Cortex-M3 Processor Applications
Low-cost microcontrollers:
  The Cortex-M3 processor is ideally suited for low-cost microcontrollers, which are commonly used in consumer products, from toys to electrical appliances.
Automotive:
  Another ideal application for the Cortex-M3 processor is in the automotive industry. The Cortex-M3 processor has very high-performance efficiency and low interrupt latency, allowing it to be used in real-time systems.
Data communications:
  The processor’s low power and high efficiency, coupled with instructions in Thumb-2 for bit-field manipulation, make the Cortex-M3 ideal for many communications applications, such as Bluetooth and ZigBee.
Industrial control:
  In industrial control applications, simplicity, fast response, and reliability are key factors.
Consumer products:
  In many consumer products, a high-performance microprocessor (or several of them) is used.

## Slide 13: Overview of the Cortex-M3

## Slide 14: Fundamentals
A simplified view of the Cortex-M3
  32-bit microprocessor

## Slide 15: What Study with Cortex-M3
Timers
Central
Processing
Unit
Software
Hardware
Internal
External
Input
System Buses
AHB/APB
ldr (read)
str (write)
ISA
USART
DAC/ADC
Internal &
External
Memory
GPIO/INT
Output
Interrupt
Compare
Capture
I2C
SPI
UART
ADC
DAC
C
Assembly
Machine Code
Interrupts
bl (interrupt)
EMC

## Slide 16: Fundamentals
Registers
Operation Modes
Built-in Nested Vectored Interrupt Controller
Memory Map
Bus Interface
Instruction Set
Interrupt and Exception

## Slide 17: Registers
Cortex-M3 has registers R0 through R15

## Slide 18: Registers
R0-R12:General Purpose Registers
  R0–R12 are 32-bit general-purpose registers for data operations
  The R0 through R7 general purpose registers are also called low registers
  The R8 through R12 registers are also called high registers
R13: Stack Pointers
  In the Cortex-M3 processor, there are two SPs.
  This duality allows two separate stack memories to be set up.
  Main Stack Pointer (MSP)
    This is the default SP
    used by the operating system (OS) kernel, exception handlers, and all application codes that require privileged access
  Process Stack Pointer (PSP)
  used by the base-level application code

## Slide 19: Registers
Stack PUSH and POP
  It is simply part of the system memory, and a pointer register (inside the processor) is used to make it work as a first-in/last-out buffer.
  The common use of a stack is to save register contents before some data processing and then restore those contents from the stack after the processing task is done

## Slide 20: Registers
R14: The Link Register
  When a subroutine is called, the return address is stored in the link register.
R15: The Program Counter
  The program counter is the current program address.
Special Registers
  Program Status registers (PSRs)
  Interrupt Mask registers (PRIMASK, FAULTMASK, and BASEPRI)
  Control register (CONTROL)

## Slide 21: Operation Modes
The Cortex-M3 processor has two modes and two privilege levels
  Thread mode and handler mode
  The operation modes determine whether the processor is running a normal program or running an exception handler like an interrupt handler or system exception handler
  When the processor is running a main program (thread mode), it can be either in a privileged state or a user state, but exception handlers can only be in a privileged state.

## Slide 22: Interrupt Controller
Cortex-M3 processor includes an interrupt controller called the Nested Vectored Interrupt Controller (NVIC)
Features
  Nested interrupt support
    All the external interrupts and most of the system exceptions can be programmed to different priority levels.
    When an interrupt occurs, the NVIC compares the priority of this interrupt to the current running priority level.
  Vectored interrupt support
    When an interrupt is accepted, the starting address of the interrupt service routine (ISR) is located from a vector table in memory.

## Slide 23: Interrupt Controller
Features
  Dynamic priority changes support
    Priority levels of interrupts can be changed by software during run time.
  Reduction of interrupt latency
    Reduction of latency features such as automatic saving and restoring some register contents, reducing delay in switching from one ISR to another, and handling of late arrival interrupts.
  Interrupt masking
    Interrupts and system exceptions can be masked based on their priority level or masked completely using the interrupt masking registers

## Slide 24: Memory Map
The Cortex-M3 has a predefined memory map
  This allows the built-in peripherals, such as the interrupt controller and the debug components, to be accessed by simple memory access instructions.
  Thus, most system features are accessible in C program code.

## Slide 25: The Bus Interface
Several bus interfaces on the Cortex-M3 processor
  Code memory buses
    The code memory region access is carried out on the code memory buses
    Two code memory buses: I-Code and D-Code
  System bus
    used to access memory and peripherals
  Private peripheral bus
    provides access to a part of the system-level memory dedicated to private peripherals, such as debugging components.

## Slide 26: Instruction Set
In previous ARM processors, the CPU had two operation states: a 32-bit ARM state and a 16-bit Thumb state.
The Cortex-M3 supports the Thumb-2 instruction set.
  It is now possible to handle all processing requirements in one operation state.
  There is no need to switch between the two instruction sets
  No need to separate ARM code and Thumb code source files, making software development and maintenance easier
  It’s easier to get the best efficiency and performance, in turn making it easier to write software

## Slide 27: Instruction Set
The Cortex-M3 processor has a number of interesting and powerful instructions
  UFBX, BFI, and BFC
    Bit field extract, insert, and clear instructions
  UDIV and SDIV
    Unsigned and signed divide instructions
  WFE, WFI, and SEV
    Wait-For-Event, Wait-For-Interrupts, and Send-Event
    These allow the processor to enter sleep mode and to handle task synchronization on multiprocessor systems
  MSR and MRS
    Move to special register from general-purpose register and move special register to general-purpose register; for access to the special registers

## Slide 28: ARM Instruction Set Architecture
32-bits
32-bits
Endianess
mov r0, #4
ldr r1, [r0,#8]
r1=mem((r0)+8)
bne loop
subs r2, #1
Endianess

## Slide 29: Interrupt and Exception
The Cortex-M3 processor implements a new exception model
  a number of system exceptions plus a number of external Interrupt Request(IRQ)
  no fast interrupt (FIQ)

## Slide 30: Summary
Introduce basic computer architecture
Microprocessor & microcontroller
ARM process development
Basic of ARM Cortex-M3
  Registers
  Interrupt
  Memory map
  Instruction set